## Slide 1: SPATIO-TEMPORAL SHORELINE PREDICITION AND VULNERABILITY ASSESSMENT ALONG THE PARTS OF COROMONDAL COAST, INDIA
Ms. MIRA SHIVANI S and Dr. N N Salghuna
Geological Technology and Geo-Informatics
Bharathidasan University
Tiruchirappalli, Tamil Nadu, India

## Slide 2: INTRODUCTION
The shoreline is a quite narrow, linear in extent and always in contact with the estuarine waterbody or Sea.
Monitoring the changes will help us to identify the root cause, human impacts and to generate measures that has to be taken to prevent further impacts.
Remote sensing data could be used to monitor the shoreline changes along the coastal zone.

## Slide 3: PURPOSE
  The aim of the study is to predict the shoreline and assess the Vulnerability for the area.
  Also, Coastal zones are extremely dynamic in nature, so understanding the cause would be a great opportunity to take measures and prevent future Disasters.

## Slide 4: STUDY AREA

## Slide 5: METHODOLOGY
SOI TOPOSHEET (1972)
LANDSAT-5 TM DATA (1990)
LANDSAT -8 OLI DATA (2020)
SHORELINE DIGITIZATION
TRANSECTS FOR 1 KM
DETERMINING COASTAL VULNERBILITY PARAMETERS USING SRTM DATA AND COLLATERAL SOURCES, COMPUTATION OF CVI
CALCULATING EROSION/ACCRETION VALUES
RANKING CVI
CVI MAP
OPEN SHEETS
PREDICTION

## Slide 6
DIGITIZED SHORELINE
1972
1990
2020

## Slide 7
CREATING TRANSECTS
1972
1990
2020

## Slide 8
DEM (SRTM DATA)
SLOPE

## Slide 9
BUFFERED FOR 900 Meters

## Slide 10
GEOMORPHOLOGY

## Slide 11
CVI | LEVEL | VALUE
16 - 18 | Very Low (VL) | 1
19 - 21 | Low (L) | 2
22 - 24 | Moderate (M) | 3
25 - 27 | High (H) | 4
28 - 30 | Very High (VH) | 5
RANKING CVI
GEOMORPHOLOGY | CVI VALUE
COASTAL PLAIN DEEP | 4
BEACH | 2
SLOPE | CVI VALUE
0 | 1
0-1 | 2
1-2 | 3
2-2.5 | 4
2.5-3 | 5
SEA LEVEL RISE | CVI VALUE
0.987 Meters | 4
MEAN TIDAL RANGE | CVI VALUE
2.3 Meters | 4
MEAN WAVE HEIGHT | CVI VALUE
3.26 Meters | 4
EROSION/ACCRETION | CVI VALUE
>1 | 1
0-(-75) | 2
-75-(-100) | 3
-100-(-160) | 4
>-160 | 5

## Slide 12
CVI MAP

## Slide 13
S.NO | 1972-1990 | 1990-2020
0 | -168.71 | -14.22
1 | -122.82 | -78.55
2 | -132.94 | -91.87
3 | -112.98 | -193.92
4 | -133.97 | -199.65
5 | -111.12 | -397.88
6 | -179.03 | 328.78
7 | -163.85 | 252.83
8 | -74.32 | 220.65
9 | -91.61 | -188.93
10 | -141.89 | -171.52
11 | -135.94 | -158.79
12 | -120.95 | -142.85
13 | -103.33 | -126.77
14 | -137.87 | -110.91
15 | -160.35 | -95.56
16 | -121.79 | -81.74
17 | -114.92 | -75.42
18 | -90.22 | -61.96
19 | -91.88 | -50.49
20 | -118.35 | 7.8
EROSION/ACCRETION VALUES
- : EROSION
+ : ACCRETION
Chart: EROSION - ACCRETION
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
1972-1990 | -168.71 | -122.82 | -132.94 | -112.98 | -133.97 | -111.12 | -179.03 | -163.85 | -74.32 | -91.61 | -141.89 | -135.94 | -120.95 | -103.33 | -137.87 | -160.35 | -121.79 | -114.92 | -90.22 | -91.88 | -118.35
1990-2020 | -14.22 | -78.55 | -91.87 | -193.92 | -199.65 | -397.88 | 328.78 | 252.83 | 220.65 | -188.93 | -171.52 | -158.79 | -142.85 | -126.77 | -110.91 | -95.56 | -81.74 | -75.42 | -61.96 | -50.49 | 7.8

## Slide 14
S.NO | 1990-2020 | 2020 - 2050
0 | -14.22 | -3.618
1 | -78.55 | -7.464
2 | -91.87 | -14.263
3 | -193.92 | -274.860
4 | -199.65 | -265.330
5 | -397.88 | -684.640
6 | 328.78 | 507.810
7 | 252.83 | 416.680
8 | 220.65 | 294.970
9 | -188.93 | -286.250
10 | -171.52 | -201.150
11 | -158.79 | -181.640
12 | -142.85 | -164.750
13 | -126.77 | -150.210
14 | -110.91 | -83.950
15 | -95.56 | -30.770
16 | -81.74 | -41.690
17 | -75.42 | -35.920
18 | -61.96 | -33.700
19 | -50.49 | -41.390
20 | 7.8 | 9.959
Chart: PREDICTION
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
1990-2020 | -14.22 | -78.55 | -91.87 | -193.92 | -199.65 | -397.88 | 328.78 | 252.83 | 220.65 | -188.93 | -171.52 | -158.79 | -142.85 | -126.77 | -110.91 | -95.56 | -81.74 | -75.42 | -61.96 | -50.49 | 7.8
2020 - 2050 | -3.6182 | -7.4639 | -14.2626 | -274.86 | -265.33 | -684.64 | 507.81 | 416.68 | 294.97 | -286.25 | -201.15 | -181.64 | -164.75 | -150.21 | -83.95 | -30.77 | -41.69 | -35.92 | -33.7 | -41.39 | 9.959

## Slide 15: RESULTS AND CONCLUSION
With the prediction done for the Puducherry Coast, it is evident that there will be more Erosion than Accretion along the coast.
Engineering structures like Groynes, Jetties, Breakwaters, Revetments can prevent the erosion along the coast.